1-Oct-04

# Emu Trigger Issues

- Trigger Primitive Conditions:

|  | Chamber HV (kV) | ME1/1 HV (kV) | AFEB Thresh. (DAC) | Compar. Thresh. (mV) | ALCT-CLCT match window (bx) | ALCT-L1A match window (bx) | TMB-L1A match window (bx) | CLCT trigger layers | ALCT trigger layers | ALCT accel. muons | Triggers per spill |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current | 3.55 | 2.95 | 20 | 40 | 5 | 3 | 5 | 4/1 | 2/4 | OFF(2) | ~300 |
| TB2003 “best” | 3.55-3.60 | X | “lowest” | 20-40 | 3 | 5 | 5 | 3/1 | 2/4 | OFF | 500-5000 |
| TB2004A | 3.55 | ? | 20 | 30 | 5 | 5 | 5 |  | varied | varied | 5-10K |

- Diagnostics:

  - Tumanov feedback

  - Bobby efficiencies

    - Can they be separated by category (matched, ALCT-only, CLCT-only)?

  - “Excellent event” efficiencies

  - Event display – RootEventDisplay

  - DQM (Cavanaugh)

  - Mumford histograms

- Should do ALCT fine-delay scans soon (may need to adjust other timings)

- Why is DDU readout so fragile? Try reset before running (NO). Find one fiber connected to a bad channel (YES!).

- ALCT ghosts? Expect few % with current settings (collision-only patterns).

- Putting in the RAT board and new backplane: when, which chamber? The one with highest efficiency. Re-timing will be needed for that chamber.

- Equalizing arrival of all LCTs at SP: done in the TMB, hard-coded at the moment.

- Special issues for ME1/1:

  - Is the ALCT firmware up-to-date? With bugs tracks are not straight – take 2/2 patterns??

  - Is the front type of chamber the right one? Both ME1/1 are the “front” type.

- What beam conditions to request? Do we want muons-only? Energy? Will have 150 GeV muons after about 10 a.m. tomorrow.

- Will it be possible to “flick a switch” to do SP triggering versus hodoscope triggering? Expect ~1 bx time slop.

- Do we see funny effects on L1A? Do we need to make our pulse to TTC longer than 25 ns to be sure to “catch it”?  Yes, with the HCAL trigger board – it is edge-triggered.