# Emu Trigger/DAQ Issues – 2-Oct-04

- Trigger Primitive Conditions:

|  | Chamber HV (kV) | ME1/1 HV (kV) | AFEB Thresh. (DAC) | Compar. Thresh. (mV) | ALCT-CLCT match (bx) | ALCT-L1A match (bx) | TMB-L1A match (bx) | CLCT trigger layers | ALCT trigger layers | ALCT accel. muons | Triggers per spill |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current | 3.65 (was 3.55) | 3.00 (was 2.95) | 20 | 30 | 5 | 3 | 5 | 4/1 | 2/4 & 2/2 | OFF(2) | ? |
| TB2003 “best” | 3.55-3.60 | X | “lowest” | 20-40 | 3 | 5 | 5 | 3/1 | 2/4 | OFF | 500-5000 |
| TB2004A | 3.55 | ? | 20 | 30 | 5 | 5 | 5 |  | varied | varied | 5-10K |

- Progress since yesterday:

  - DDU bad fiber input swapped to good one, 5 chambers now being read out (bug fixes).

  - High voltages were raised for better efficiency.

  - ME1/1 ALCT coincidences changed from 4 planes to 2 for high efficiency.

  - Front (HCAL) ME1/1 chamber ALCT data shut off in TMB.

  - Comparator thresholds lowered from 40 mV to 30 mV.

- Notes:

  - DQM bug sees 2x the true number of CLCTs.

  - ME2/2 tripped off at one point, only reset when set to 10v and then raised.

- DQM (Cavanaugh) assessment of present status of chambers/paths during run 112-3:

|  | Downstream ME1/1 (CSCID 2) | ME1/2 (8) | ME2/2 (3) | ME3/2 (9) | Upstream ME1/1 (?) |
| --- | --- | --- | --- | --- | --- |
| DDU Events | ( | ( | ( | ( | ? |
| DMB Found | ( | ( | ( | ( | ? |
| ALCT Found | ( 23% | ( | ( | ( | ? |
| CLCT Found | ( 75% | ( | ( | ( | ? |
| CFEB Found | ( | ( | ( | ( | ? |

- Other diagnostics:

  - Tumanov feedback

  - DQM (Cavanaugh)

  - SP efficiencies (Bobby): Can they be separated (matched, ALCT-only, CLCT-only)?

  - Event display – RootEventDisplay

  - Mumford histograms

- Next steps:

  - Move all efficiencies close to 100%. If not, try adjusting 3 bx to 5 bx coincidence windows.

  - Put in HCAL trigger board interface to L1A soon, check timing OK. (Our coincidence should be >25 ns long to make sure it’s latched by the trigger board.

  - Then do ALCT fine-delay scans soon (may need to adjust other timings)

  - Equalizing arrival of all LCTs at SP: done in the TMB, hard-coded at the moment.

  - Equalizing BXN numbers by changing offsets in ALCT, TMB, DMB, DDU.

  - Putting in the RAT board and new backplane, re-timing in.

- Later steps:

  - Worry about handling of BC0 between different modules (relevant only for structured beam?)

  - Get better ME1/1 ALCT firmware from Madorsky.

  - Try Darin’s file with ALCT “B” configuration turned off, only collision muons.

  - Accommodate changed RPC link board output format.

  - Install full “final” peripheral crate backplane when it arrives.