# Emu Trigger/DAQ Issues: 3-Oct-04

- Trigger Primitive Conditions:

|  | Chamber HV (kV) | ME1/1 HV (kV) | AFEB Thresh. (DAC) | Compar. Thresh. (mV) | ALCT-CLCT match (bx) | ALCT-L1A match (bx) | TMB-L1A match (bx) | CLCT trigger layers | ALCT trigger layers | ALCT accel. muons | Triggers per spill |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current | 3.65 (was 3.55) | 3.00 (was 2.95) | 20 | 30 | 5 | 3 | 5 | 4/1 | 2/4 & 2/2 | OFF(2) | 1400 gated (6000 raw) |
| TB2003 “best” | 3.55-3.60 | X | “lowest” | 20-40 | 3 | 5 | 5 | 3/1 | 2/4 | OFF | 500-5000 |
| TB2004A | 3.55 | ? | 20 | 30 | 5 | 5 | 5 |  | varied | varied | 5-10K |

- Progress since yesterday:

  - Front (HCAL) ME1/1 chamber ALCT cables were swapped (possible short), now the data looks good.

  - All chambers’ efficiencies (ALCT, CLCT, CFEB, DMB, DDU) look good (typically 99.8%).

  - We’re now taking saved data (runs >=400).

  - Fine delay scan for ALCTs taken – results?

  - SP is finding tracks and output is now in parallel to scintillator in terms of L1A generation.

  - New crate with new backplane and RAT board rear readout (Dynatem was flashed) set up with ME3/2 and getting timed in.

  - chambers have all been moved to CSCids >3 (see online logbook) which should make offline tracking more consistent.

- Notes:

  - Problems with data corruption from new DDU – problem with driver?

    - occasional (after a spil?) a single event gets corrupted probably partially overwritten. Investigating

  - Analysis jobs are having trouble with new DDU runs as well.

- DQM (Cavanaugh) assessment of present status of chambers/paths during run 401:

|  | Downstream ME1/1 (CSCID 2) | ME1/2 (8) | ME2/2 (3) | ME3/2 (9) | Upstream ME1/1 |
| --- | --- | --- | --- | --- | --- |
| DDU Events | ( | ( | ( | ( | ( |
| DMB Found | ( | ( | ( | ( | ( |
| ALCT Found | ( | ( | ( | ( | ( |
| CLCT Found | ( | ( | ( | ( | ( 87% |
| CFEB Found | ( | ( | ( | ( | ( |

- Next steps:

  - Put in HCAL trigger board interface to L1A soon, check timing OK. (Our coincidence should be >25 ns long to make sure it’s latched by the trigger board.

  - Set ALCT fine-delay scans properly – waiting for analysis results.

  - Equalizing arrival of all LCTs at SP: done in the TMB, hard-coded at the moment.

  - Equalizing BXN numbers by changing offsets in ALCT, TMB, DMB, DDU.

  - Putting in the RAT board and new backplane, re-timing in.

- Later steps:

  - Worry about handling of BC0 between different modules (relevant only for structured beam?)

  - Get better ME1/1 ALCT firmware from Madorsky.

  - Try Darin’s file with ALCT “B” configuration turned off, only collision muons.

  - Accommodate changed RPC link board output format.

  - Install full “final” peripheral crate backplane when it arrives.