# Emu Trigger/DAQ Issues: 4-Oct-04

- No beam today – switch-over to synchronized beam.

- Trigger Primitive Conditions:

  - Only change from yesterday: comparator delay=1 in ME3/2 rather than 0 in others, since CFEB timing of this chamber changed when moved to new crate, since we have to use the old CCB2001 which is apparently slower at passing signals through it.

- Progress since yesterday:

  - Fine delay scan for ALCTs analysis shows strange results for most chambers.

  - SP is finding tracks and output is now in parallel to scintillator in terms of L1A generation.

  - New crate with new backplane and RAT board rear readout (Dynatem was flashed) set up with ME3/2 and was timed in.

  - Chambers have all been moved to CSCids >3 (see online logbook) which should make offline tracking more consistent.

- Notes:

  - Problems with data corruption from new DDU:

    - occasional (after a spill?) a single event gets corrupted probably partially overwritten. We can run without errors if we re-start the BigPhys drivers every run.

  - Analysis jobs are still having some trouble with new DDU runs as well – some progress tho.

  - XDAQ “Emu live feed” under development, Rick Wilkinson is looking for why it crashes.

- DQM (Cavanaugh) assessment of present status of chambers/paths during run 401:

|  | Downstream ME1/1 (CSCID 2) | ME1/2 (8) | ME2/2 (3) | ME3/2 (9) | Upstream ME1/1 |
| --- | --- | --- | --- | --- | --- |
| DDU Events | ( | ( | ( | ( | ( |
| DMB Found | ( | ( | ( | ( | ( |
| ALCT Found | ( | ( | ( | ( | ( |
| CLCT Found | ( | ( | ( | ( | ( 87% |
| CFEB Found | ( | ( | ( | ( | ( |

- Next steps:

  - Re-take ALCT fine-delay scans to get more reasonable results?

  - Equalizing arrival of all LCTs at SP, done in the TMB (addr B2 bits [11:08]):

    - ME2/2 is currently BX 2, ME1/2 is BX 3, ME1/1 is BX 4. Delay ME2/2 by 2 bx and ME1/2 by 1 bx to equalize.

  - Download new ME1/1 ALCT firmware with correct wire mapping when it arrives from Madorsky.

  - Mike Matveev will route specific chambers to specific MPC output links to make SP job easier.

  - Equalizing BXN numbers by changing offsets in ALCT (not documented?), TMB (Adr 76 bits [15:04]), DMB (recompile firmware), DDU.

- Later steps:

  - Have TMB forward BC0 even when no data (firmware change).

  - Worry about handling of BC0 between different modules (relevant only for structured beam?)

  - Try Darin’s file with ALCT “B” configuration turned off, only collision muons.

  - Accommodate changed RPC link board output format.

  - Install full “final” peripheral crate backplane when it arrives.