# Emu Trigger/DAQ Issues: Wednesday 6-Oct-04

- Synchronized beam.

- Trigger Primitive Conditions:

|  | Chamber HV (kV) | ME1/1 HV (kV) | AFEB Thresh. (DAC) | Compar. Thresh. (mV), mode, delay | ALCT-CLCT delay, match (bx) | ALCT-L1A delay, match (bx) | TMB-L1A delay, match (bx) | DMB ALCT, CLCT data delays | CLCT trigger layers | ALCT trigger layers | ALCT accel. muons | Triggers per spill |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current | 3.65 | 3.00 | 20 | 30, 2?, 0? | ,5 | ,3 | ,5 |  | 4/1 | 2/4 & 2/2 | OFF(2) |  |
| TB2003 “best” | 3.55-3.60 | X | “lowest” | 20-40, ?, ? | 3 | 5 | 5 |  | 3/1 | 2/4 | OFF | 500-5000 |
| TB2004A | 3.55 | ? | 20 | 30, ?, ? | 5 | 5 | 5 |  |  | varied | varied | 5-10K |

- Just in (as of ~22:00 Oct. 6): DMB has been resetting our finely tuned constants when the TTC config. and TTC enable scripts were run, because it cleared everything on a sync-reset. This was a bug that Jianghu has now fixed in the DMB firmware. Argh – this has been messing up our timing for the last 3 days!

- Changes from Oct 4:

  - New ALCT firmware installed with correct (?) wire order in ME1/1 and ability to change BXN offset.

  - New TMB firmware installed with: send BC0 to MPC regardless of LCT triggering, switch to reset BXN either with only BXRESET (default) or with BC0, also ability to trigger internal scope on CRC-error from ALCT.

  - Jianghu updated DMB firmware on ME1/1 (HCAL) and ME3/2.

  - Dynatem on ME1/1 (HCAL) crate pushed in all the way, CCB on ME3/2 changed from CCB2001 to CCB2004.

- Progress since Oct 4:

  - Data corruption from DDU seems to related to incomplete reset procedure, so before starting run need to completely reset drivers.

  - Analysis jobs can now run on new DDU data, and some can distinguish between 2 chambers with CSCID=6.

  - XDAQ “Emu live feed” and combined HCAL-EMU run software done and (8!) events taken.

  - MPC transparent mode (specific links for specific chambers/muons, rather than sorting) may be working (configuration software bug fix).

- Notes:

- Status as of Weds. Oct. 6 day shift according to DQM

|  | Downstream ME1/1 (CSCID 2) | ME1/2 (8) | ME2/2 (3) | ME3/2 (9) | Upstream ME1/1 |
| --- | --- | --- | --- | --- | --- |
| DDU Events | ( | ( | ( | ( | ( |
| DMB Found | ( | ( | ( | ( | ( |
| ALCT Found | ( | ( | ( | ( | ( 7% |
| CLCT Found | ( | ( | ( | ( 85% | ( 90% |
| CFEB Found | ( | ( | ( | ( 50% | ( 1% |

- Next steps:

  - SP: run check for orbit structure: is it always 48 bx with particles out of 924?

  - Get rid of sync resets between spills (Florida TTC configuration script).

  - Re-run the ALCT timing curves again.

  - Install full “final” peripheral crate backplane in preparation for RPC data.

  - Fix up ME1/1 (HCAL) ALCT timing.

  - Equalizing arrival of all LCTs at SP

- Later steps:

  - Try Darin’s file with ALCT “B” configuration turned off, only collision muons.