# Emu Trigger/DAQ Issues: Wednesday 7-Oct-04

- Synchronized beam.

- Trigger Primitive Conditions:

|  | Chamber HV (kV) | ME1/1 HV (kV) | AFEB Thresh. (DAC) | Compar. Thresh. (mV), mode, delay | ALCT-CLCT match (bx) | ALCT-L1A match (bx) | TMB-L1A match (bx) | CLCT trigger layers | ALCT trigger layers | ALCT accel. muons | Triggers per spill |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Current | 3.65 | 3.00 | 20 | 30 | 5 | 3 | 5 | 4/1 | 2/4 & 2/2 | OFF(2) | varies |
| TB2003 “best” | 3.55-3.60 | X | “lowest” | 20-40 | 3 | 5 | 5 | 3/1 | 2/4 | OFF | 500-5000 |
| TB2004A | 3.55 | ? | 20 | 30 | 5 | 5 | 5 |  | varied | varied | 5-10K |

- Changes from yesterday:

  - Since DMB bug fix, trigger adjustments work fine (whew!)

  - Fine timing done for all chambers.

  - ALCT-CLCT coincidence windows adjusted.

  - Equalized arrival of LCTs at input to SP.

- Progress since yesterday:

  - Combined HCAL-Emu readout took hundreds of thousands of events. However, SP trigger wasn’t actually being triggered on except for SP readout.

  - SP test of orbit structure looks good. (bx counter reset every orbit)

  - ALCT versus CLCT bunch structure looks bad in DQM – several groups of 48-bx data. Need to understand.

- Notes:

  - Run 472 (5 spills) perfect trigger primitives.

  - Run 470 (5 spills) good, but timing ever so slightly off.

- Status as of Thurs. Oct. 7 at 13:00 according to DQM

|  | Downstream ME1/1 (CSCID 2) | ME1/2 (8) | ME2/2 (3) | ME3/2 (9) | Upstream ME1/1 |
| --- | --- | --- | --- | --- | --- |
| DDU Events | ( | ( | ( | ( | ( |
| DMB Found | ( | ( | ( | ( | ( |
| ALCT Found | ( | ( | ( | ( | ( |
| CLCT Found | ( | ( | ( | ( | ( |
| CFEB Found | ( | ( | ( | ( | ( |

- Next steps:

  - Make sure SP trigger gives L1A that doesn’t change the overall timing (adjust at CCB).

  - Take long runs with good timing, esp with DDU and SP.

  - Time in winner bits for the Muon Sorter.

  - Turn on and off transparent mode of the MPC.

  - Resurrect Emu Run_Control

  - Install full “final” peripheral crate backplane in preparation for RPC data (Mike Matveev).

- Later steps:

  - Do a multi-SP to Muon Sorter run.

  - Add RPC Link board inputs to TMB readout (Saturday).

  - Try Darin’s file with ALCT “B” configuration turned off, only collision muons.